| INTENDED USE This cable guardrail anchor is for use with the SGR01 cable guardrail. The slip-base post is designed to release at the base in an end-on impact. The notches in the FPA02 bracket allow the cables to disengage in a frontal impact while providing adequate anchoring capability in downstream impacts. SEC01 is a Test Level 3 system. COMPONENTS The concrete anchor block may be cast-in-place as one piece or precast in two pieces, one to support the breakaway post and the other for the cable anchor. Concrete shall develop a 28-day strength of not less than 4000 psi [28 MPa]. The concrete shall use a cement conforming to AASHTO M85 Type I or II. Unit length = 288 inches [7500 mm] Designator Component Number POF03 Anchor foundation assembly (includes 1 PSE06) 1 PSE01 Line posts 2 RCE01 Turnbuckle and spring compensator 3 RCE03 Cable end fitting, nut washers and cable 3 RCM01 Cable (end of main guardrail run) 3 APPROVALS FHWA Acceptance Letter CC-63, 2/14/00. REFERENCES R.G. Phillips, A.B. Tyrell, J.E. Bryden and J.S. Fortuniewicz, Cable Guiderail Breakaway Terminal Ends, Engineering Research and Development Bureau, New York Department of Transportation, FHWA Report FHWA/NY/RR-90/148, Albany, NY, March 1990. CONTACT INFORMATION Federal Highway Administration Office of Safety 400 Seventh Street, SW Washington, DC 20590 202-366-2288 |
| --- |
| CABLE GUARDRAIL ANCHOR |
| SEC01 |  |
| SHEET NO. | DATE |  |
| 2 of 4 | 8/11/05 |  |

| This sheet intentionally left blank. |
| --- |
| CABLE GUARDRAIL ANCHOR |
| SEC01 |  |
| SHEET NO. | DATE |  |
| 4 of 4 | 8/11/05 |  |